## Slide 1: Visual Interface for Wi-Fi Networks Monitoring
FERRAN SELVA RODRÍGUEZ
Bachelor‘s Degree in telematics engineering
DIRECTOR: JAUME BARCELÓ

## Slide 2: OUTLINE
INTRODUCTION
STATE OF THE ART
SYSTEM COMPONENTS
SYSTEM OPERATION
TESTING THE SYSTEM
CONCLUSIONS
FUTURE WORK

## Slide 3: INTRODUCTION
Idea:
This thesis aims at providing a tool to monitor the status of the access points of “Barcelona WiFi” and share this information with the citizens

## Slide 4: INTRODUCTION
Bottom Up Broadband (BuB):
  Defines network design, deployment and operation initiatives driven by end user needs
  The individuals, companies or institutions that need the network are the ones that take the initiative and participate in the organization and funding of the project
  Difficulties: Agreement among the many parts
  Advantages: Deploy networks in regions that are not attractive to commercial operators.

## Slide 5: State of the Art
Gowex:
  Spanish telecommunication company
  Deploys Wi-Fi networks for the cities
  Present over 80 cities, like Madrid, Miami or New York
  Last New: Gowex File for Insolvency; CEO Quits on
  Fake Accounts [El Mundo. Jul 6, 2014 ]
Existing monitoring software:
  Pandora FMS
  PRTG Network Monitor
  Nagios
  Munin

## Slide 6: State of the Art
Guifi.net tools:
  Web Application / qMp: Status and traffic
  Munin
  Nagios
Barcelona Wifi tools:
  Public Information: Location
  Private Information: Google Earth application
    Status
    Location
    Current number of Users
    Current number of jumps until the Gateway

## Slide 7: SYSTEM COMPONENTS
Raspberry Pi
Server
Access Points
HARDWARE COMPONENTS
SOFTWARE COMPONENTS
Access (Java Application)
Web Application
MongoDB Database
Web service

## Slide 8: SYSTEM COMPONENTS Hardware COMPONENTS
Raspberry Pi
  Credit-Card sized computer
  Model B Ethernet
  Auto-run the Access java application when it is booted
Figure 1: Raspberry Pi

## Slide 9: SYSTEM COMPONENTS Hardware COMPONENTS
Server
  Universitat Pompeu Fabra Server
  Apache HTTP Provides access to web applications
  MongoDB Database stores the data

## Slide 10: SYSTEM COMPONENTS Hardware COMPONENTS
Access Point
  Devices whose performance is being monitored
Figure 2: Linksys WRT54Gt Access Point

## Slide 11: SYSTEM COMPONENTS SOFTWARE COMPONENTS
Access (Java Application)
  Main goal: Updates the status of the access point to be monitored
  Written in Java
  Executed at the Raspberry Pi
  Methodology:
Get the needed Data to ping the Access Points
Get the Response
Process this information
Send the information to the Database
Ping the Access Points

## Slide 12: SYSTEM COMPONENTS SOFTWARE COMPONENTS
Web Application
Main goal: Displays the information about the status of the access points
Written in HTML, Javascript and PHP
Located at the server
Figure 3: Web Application

## Slide 13: SYSTEM COMPONENTS SOFTWARE COMPONENTS
MongoDB Database (1)
  Main goal: Stores the information obtained by the Access java application
  Collections:
    Resume Stores for each Access Point the following data:
  ID
  IP
  Latitude
  Longitude
  Status
  Since
  Totaltime
  Uptime
  Downtime
  Availability

## Slide 14: SYSTEM COMPONENTS SOFTWARE COMPONENTS
MongoDB Database (2)
    Data A register is stored each time that the Access java application tries to ping an Access Point.
    The information stored at each register is:
  ID
  Status
  Timestamp

## Slide 15: SYSTEM COMPONENTS SOFTWARE COMPONENTS
Web service
  Main goal: provides a way of communication between the Access java application at the Raspberry Pi and MongoDB Database at the server
  Written in PHP
  Located at the Server

## Slide 16: SYSTEM OPERATION
Figure 4: System Diagram

## Slide 17: TESTING THE SYSTEM Test
Network: Poblenou Sense Fils.
  Location: Barcelona
  Number of nodes: 45
  Duration: 5 Days.
Location of the Raspberry Pi: Tanger building of the Universitat Pompeu Fabra.

## Slide 18: TESTING THE SYSTEM RESULTS
Database Results
        Collection Size:
    Data: + 2.070.792 Bytes
    Resume: + 320 Bytes
        Document Size:
    Data: +104’76 Bytes
    Resume: + 7,11 Bytes
        Number of Documents:
    Data: 45 Documents
    Resume: + 19.766 Documents
Table 1: Summary Table of Collections Stats

## Slide 19: TESTING THE SYSTEM RESULTS
Mailing
        Address: bub.project.apcontrol@gmail.com
        Number of email received: 223 emails
Processing the Information
        TOTALTIME: 5 days=120 hours BCNgranvia940AH =119’71
Unexpected stops
        There were no unexpected stops.
        Anyway, to restart the system is easy Rebooting Raspberry Pi

## Slide 20: CONCLUSIONS
The system is simply and inexpensive
The system is compatible with all networks
The results of the test show a good performance
The simplicity leads to miss some information

## Slide 21: FUTURE WORK
SNMP Implementation (Libraries for java, like snmp4j)
  Obtain more information
  Add CONTROL capabilities
    Turn On
    Turn Off
    Reboot
    Others
Web Application Improving
  View the log of a particular access point
  Add search criteria. Options like geographical area, number of users or action point status

## Slide 22
Thank you